## Slide 1: CS252 Graduate Computer Architecture Lecture 6 Scoreboard, Tomasulo, Register Renaming February 7th, 2011
John Kubiatowicz
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~kubitron/cs252

## Slide 2: Recall: Revised FP Loop Minimizing Stalls
6 clocks: Unroll loop 4 times code to make faster?
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
1 Loop: LD F0,0(R1)
2 stall
3 ADDD F4,F0,F2
4 SUBI R1,R1,8
5 BNEZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;altered when move past SUBI
Swap BNEZ and SD by changing address of SD
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 3: Recall: Software Pipelining Example
Before: Unrolled 3 times
1 LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12
10 SUBI R1,R1,#24
11 BNEZ R1,LOOP
After: Software Pipelined
1 SD 0(R1),F4 ; Stores M[i]
2 ADDD F4,F0,F2 ; Adds to M[i-1]
3 LD F0,-16(R1); Loads M[i-2]
4 SUBI R1,R1,#8
5 BNEZ R1,LOOP
Symbolic Loop Unrolling
Maximize result-use distance
Less code space than unrolling
Fill & drain pipe only once per loop vs. once per each unrolled iteration in loop unrolling
SW Pipeline
Loop Unrolled
overlapped ops
Time
Time
5 cycles per iteration

## Slide 4: Can we use HW to get CPI closer to 1?
Why in HW at run time?
  Works when can’t know real dependence at compile time
  Compiler simpler
  Code for one machine runs well on another
Key idea: Allow instructions behind stall to proceed DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14
Out-of-order execution => out-of-order completion.

## Slide 5: Problems?
How do we prevent WAR and WAW hazards?
How do we deal with variable latency?
  Forwarding for RAW hazards harder.
How to get precise exceptions?
RAW
WAR

## Slide 6: Scoreboard: a bookkeeping technique
Out-of-order execution divides ID stage:
  1. Issue—decode instructions, check for structural hazards
  2. Read operands—wait until no data hazards, then read operands
Scoreboards date to CDC6600 in 1963
  Readings for Monday include one on CDC6600
Instructions execute whenever not dependent on previous instructions and no hazards.
CDC 6600: In order issue, out-of-order execution, out-of-order commit (or completion)
  No forwarding!
  Imprecise interrupt/exception model for now

## Slide 7: Scoreboard Architecture (CDC 6600)
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 8: Scoreboard Implications
Out-of-order completion => WAR, WAW hazards?
Solutions for WAR:
  Stall writeback until registers have been read
  Read registers only during Read Operands stage
Solution for WAW:
  Detect hazard and stall issue of new instruction until other instruction completes
No register renaming (next time)
Need to have multiple instructions in execution phase => multiple execution units or pipelined execution units
Scoreboard keeps track of dependencies between instructions that have already issued.
Scoreboard replaces ID, EX, WB with 4 stages

## Slide 9: Four Stages of Scoreboard Control
Issue—decode instructions & check for structural hazards (ID1)
  Instructions issued in program order (for hazard checking)
  Don’t issue if structural hazard
  Don’t issue if instruction is output dependent on any previously issued but uncompleted instruction (no WAW hazards)
Read operands—wait until no data hazards, then read operands (ID2)
  All real dependencies (RAW hazards) resolved in this stage, since we wait for instructions to write back data.
  No forwarding of data in this model!

## Slide 10: Four Stages of Scoreboard Control
Execution—operate on operands (EX)
  The functional unit begins execution upon receiving operands. When the result is ready, it notifies the scoreboard that it has completed execution.
Write result—finish execution (WB)
  Stall until no WAR hazards with previous instructions: Example: DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F8,F8,F14 CDC 6600 scoreboard would stall SUBD until ADDD reads operands

## Slide 11: Three Parts of the Scoreboard
Instruction status: Which of 4 steps the instruction is in
Functional unit status:—Indicates the state of the functional unit (FU). 9 fields for each functional unit Busy: Indicates whether the unit is busy or not Op: Operation to perform in the unit (e.g., + or –) Fi: Destination register Fj,Fk: Source-register numbers Qj,Qk: Functional units producing source registers Fj, Fk Rj,Rk: Flags indicating when Fj, Fk are ready
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions will write that register
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 12: Scoreboard Example

## Slide 13: Detailed Scoreboard Pipeline Control
Read operands
Execution complete
Instruction status
Write result
Issue
Bookkeeping
Rj No; Rk No
f(if Qj(f)=FU then Rj(f) Yes); f(if Qk(f)=FU then Rj(f) Yes); Result(Fi(FU)) 0; Busy(FU) No
Busy(FU) yes; Op(FU) op; Fi(FU) `D’; Fj(FU) `S1’; Fk(FU) `S2’; Qj Result(‘S1’); Qk Result(`S2’); Rj not Qj; Rk not Qk; Result(‘D’) FU;
Rj and Rk
Functional unit done
Wait until
f((Fj(f)Fi(FU) or Rj(f)=No) & (Fk(f)Fi(FU) or Rk( f )=No))
Not busy (FU) and not result(D)
Notes: 1.Issue - if no structural haards AND non wAW (no Funtional Unit is going to write this destination register; 1 per clock cycle
2. Read -(RAW) if no instructions is going to write a source register of this instruction (alternatively, no write signal this clock cycle) +> gein exection of the instruction; many read ports, so can read many times
3. Execution Complete; multiple during clock cyle
4. Write result - (WAR) If no instructiion is watiing to read the destination register; assume multiple wriite ports; wait for clock cycle to write and tehn read the results; assume can oerlap issue & write
show clock cyclesneed 20 or so
Latency: minimum is 4 through 4 stages

## Slide 14: Scoreboard Example: Cycle 1

## Slide 15: Scoreboard Example: Cycle 2
Issue 2nd LD?

## Slide 16: Scoreboard Example: Cycle 3
Issue MULT?

## Slide 17: Scoreboard Example: Cycle 4

## Slide 18: Scoreboard Example: Cycle 5

## Slide 19: Scoreboard Example: Cycle 6

## Slide 20: Scoreboard Example: Cycle 7
Read multiply operands?

## Slide 21: Scoreboard Example: Cycle 8a (First half of clock cycle)

## Slide 22: Scoreboard Example: Cycle 8b (Second half of clock cycle)

## Slide 23: Scoreboard Example: Cycle 9
Read operands for MULT & SUB? Issue ADDD?
Note
Remaining

## Slide 24: Scoreboard Example: Cycle 10

## Slide 25: Scoreboard Example: Cycle 11

## Slide 26: Scoreboard Example: Cycle 12
Read operands for DIVD?

## Slide 27: Scoreboard Example: Cycle 13

## Slide 28: Scoreboard Example: Cycle 14

## Slide 29: Scoreboard Example: Cycle 15

## Slide 30: Scoreboard Example: Cycle 16

## Slide 31: Scoreboard Example: Cycle 17
Why not write result of ADD???
WAR Hazard!

## Slide 32: Scoreboard Example: Cycle 18

## Slide 33: Scoreboard Example: Cycle 19

## Slide 34: Scoreboard Example: Cycle 20

## Slide 35: Scoreboard Example: Cycle 21
WAR Hazard is now gone...

## Slide 36: Scoreboard Example: Cycle 22

## Slide 37: Faster than light computation (skip a couple of cycles)

## Slide 38: Scoreboard Example: Cycle 61

## Slide 39: Scoreboard Example: Cycle 62

## Slide 40: Review: Scoreboard Example: Cycle 62
In-order issue; out-of-order execute & commit

## Slide 41: CDC 6600 Scoreboard
Speedup 1.7 from compiler; 2.5 by hand BUT slow memory (no cache) limits benefit
Limitations of 6600 scoreboard:
  No forwarding hardware
  Limited to instructions in basic block (small window)
  Small number of functional units (structural hazards), especially integer/load store units
  Do not issue on structural hazards
  Wait for WAR hazards
  Prevent WAW hazards

## Slide 42: CS 252 Administrivia
Interesting Resource: http://bitsavers.org
  Has digital versions of users manuals for old machines
  Quite interesting!
  I’ll link in some of them to your reading pages when it is appropriate
  Very limited bandwidth: use mirrors such as: http://bitsavers.vt100.net
Textbook Reading for next few lectures:
  Computer Architecture: A Quantitative Approach, Chapter 2
Midterm I: March 16th
  Currently exam on 16th is scheduled for 2:30-5:30. Would this work for people? Room is available up until 7:00, so could do 4:00-7:00.
  Pizza afterwards…

## Slide 43: Paper Discussion (Reading #4)
"Parallel Operation in the CDC 6600," James E. Thorton. AFIPS Proc. FJCC, pt. 2 vol. 03, pp. 33-40, 1964
  Pushed the Load-Store architecture that became staple of RISC
  Scoreboard for OOO execution (last lecture)
  Separation of I/O processors from main processor
    Memory-mapped communication between them
    Very modern ideas
"The CRAY-1 Computer System," Richard Russel. Communications of the ACM, 21(1) 63-72, January 1978
  Very successful Vector Machine
  Highly tuned physical implementation
  No Virtual Memory: segmented protection + relocatable code

## Slide 44: Another Dynamic Algorithm: Tomasulo Algorithm
For IBM 360/91 about 3 years after CDC 6600 (1966)
Goal: High Performance without special compilers
Differences between IBM 360 & CDC 6600 ISA
  IBM has only 2 register specifiers/instr vs. 3 in CDC 6600
  IBM has 4 FP registers vs. 8 in CDC 6600
  IBM has memory-register ops
Why Study? lead to Alpha 21264, HP 8000, MIPS 10000, Pentium II, PowerPC 604, …

## Slide 45: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 46: Tomasulo Algorithm vs. Scoreboard
Control & buffers distributed with Function Units (FU) vs. centralized in scoreboard;
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as well
Integer instructions can go past branches, allowing FP ops beyond basic block in FP queue

## Slide 47: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: No ready flags as in Scoreboard; Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 48: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast

## Slide 49: Tomasulo Example

## Slide 50: Tomasulo Example Cycle 1

## Slide 51: Tomasulo Example Cycle 2
Note: Unlike 6600, can have multiple loads outstanding

## Slide 52: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued vs. scoreboard
Load1 completing; what is waiting for Load1?

## Slide 53: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 54: Tomasulo Example Cycle 5

## Slide 55: Tomasulo Example Cycle 6
Issue ADDD here vs. scoreboard?

## Slide 56: Tomasulo Example Cycle 7
Add1 completing; what is waiting for it?

## Slide 57: Tomasulo Example Cycle 8

## Slide 58: Tomasulo Example Cycle 9

## Slide 59: Tomasulo Example Cycle 10
Add2 completing; what is waiting for it?

## Slide 60: Tomasulo Example Cycle 11
Write result of ADDD here vs. scoreboard?
All quick instructions complete in this cycle!

## Slide 61: Tomasulo Example Cycle 12

## Slide 62: Tomasulo Example Cycle 13

## Slide 63: Tomasulo Example Cycle 14

## Slide 64: Tomasulo Example Cycle 15

## Slide 65: Tomasulo Example Cycle 16

## Slide 66: Faster than light computation (skip a couple of cycles)

## Slide 67: Tomasulo Example Cycle 55

## Slide 68: Tomasulo Example Cycle 56
Mult2 is completing; what is waiting for it?

## Slide 69: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and completion.

## Slide 70: Compare to Scoreboard Cycle 62
Why take longer on scoreboard/6600?
  Structural Hazards
  Lack of forwarding

## Slide 71: Tomasulo v. Scoreboard (IBM 360/91 v. CDC 6600)
Pipelined Functional Units Multiple Functional Units
(6 load, 3 store, 3 +, 2 x/÷) (1 load/store, 1 + , 2 x, 1 ÷)
window size: ≤ 14 instructions ≤ 5 instructions
No issue on structural hazard same
WAR: renaming avoids stall completion
WAW: renaming avoids stall issue
Broadcast results from FU Write/read registers
Control: reservation stations central scoreboard

## Slide 72: Recall: Unrolled Loop That Minimizes Stalls
What assumptions made when moved code?
  OK to move store past SUBI even though changes register
  OK to move loads before stores: get right data?
  When is it safe for compiler to do such changes?
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SD -16(R1),F12
12 SUBI R1,R1,#32
13 BNEZ R1,LOOP
14 SD 8(R1),F16 ; 8-32 = -24
14 clock cycles, or 3.5 per iteration

## Slide 73: Tomasulo Loop Example
Loop: LD F0 0 R1
MULTD F4 F0 F2
SD F4 0 R1
SUBI R1 R1 #8
BNEZ R1 Loop
Assume Multiply takes 4 clocks
Assume first load takes 8 clocks (cache miss), second load takes 1 clock (hit)
To be clear, will show clocks for SUBI, BNEZ
Reality: integer instructions ahead

## Slide 74: Loop Example

## Slide 75: Loop Example Cycle 1

## Slide 76: Loop Example Cycle 2

## Slide 77: Loop Example Cycle 3
Implicit renaming sets up “DataFlow” graph

## Slide 78: Loop Example Cycle 4
Dispatching SUBI Instruction

## Slide 79: Loop Example Cycle 5
And, BNEZ instruction

## Slide 80: Loop Example Cycle 6
Notice that F0 never sees Load from location 80

## Slide 81: Loop Example Cycle 7
Register file completely detached from computation
First and Second iteration completely overlapped

## Slide 82: Loop Example Cycle 8

## Slide 83: Loop Example Cycle 9
Load1 completing: who is waiting?
Note: Dispatching SUBI

## Slide 84: Loop Example Cycle 10
Load2 completing: who is waiting?
Note: Dispatching BNEZ

## Slide 85: Loop Example Cycle 11
Next load in sequence

## Slide 86: Loop Example Cycle 12
Why not issue third multiply?

## Slide 87: Loop Example Cycle 13

## Slide 88: Loop Example Cycle 14
Mult1 completing. Who is waiting?

## Slide 89: Loop Example Cycle 15
Mult2 completing. Who is waiting?

## Slide 90: Loop Example Cycle 16

## Slide 91: Loop Example Cycle 17

## Slide 92: Loop Example Cycle 18

## Slide 93: Loop Example Cycle 19

## Slide 94: Loop Example Cycle 20

## Slide 95: Why can Tomasulo overlap iterations of loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
Other idea: Tomasulo building dynamic “DataFlow” graph from instructions
  Fits in with readings for Wednesday

## Slide 96: Explicit Register Renaming
Tomasulo provides Implicit Register Renaming
  User registers renamed to reservation station tags
Explicit Register Renaming:
  Use physical register file that is larger than number of registers specified by ISA
Keep a translation table:
  ISA register => physical register mapping
  When register is written, replace table entry with new register from freelist.
  Physical register becomes free when not being used by any instructions in progress.
Pipeline can be exactly like “standard” DLX pipeline
  IF, ID, EX, etc….
Advantages:
  Removes all WAR and WAW hazards
  Like Tomasulo, good for allowing full out-of-order completion
  Allows data to be fetched from a single register file
  Makes speculative execution/precise interrupts easier:
    All that needs to be “undone” for precise break point is to undo the table mappings

## Slide 97: Question: Can we use explicit register renaming with scoreboard?
Rename
Table
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 98: Scoreboard Example
Initialized Rename Table

## Slide 99: Renamed Scoreboard 1
Each instruction allocates free register
Similar to single-assignment compiler transformation

## Slide 100: Renamed Scoreboard 2

## Slide 101: Renamed Scoreboard 3

## Slide 102: Renamed Scoreboard 4

## Slide 103: Renamed Scoreboard 5

## Slide 104: Renamed Scoreboard 6

## Slide 105: Renamed Scoreboard 7

## Slide 106: Renamed Scoreboard 8

## Slide 107: Renamed Scoreboard 9

## Slide 108: Renamed Scoreboard 10
WAR Hazard gone!
Notice that P32 not listed in Rename Table
  Still live. Must not be reallocated by accident

## Slide 109: Renamed Scoreboard 11

## Slide 110: Renamed Scoreboard 12

## Slide 111: Renamed Scoreboard 13

## Slide 112: Renamed Scoreboard 14

## Slide 113: Renamed Scoreboard 15

## Slide 114: Renamed Scoreboard 16

## Slide 115: Renamed Scoreboard 17

## Slide 116: Renamed Scoreboard 18

## Slide 117: Explicit Renaming Support Includes:
Rapid access to a table of translations
A physical register file that has more registers than specified by the ISA
Ability to figure out which physical registers are free.
  No free registers  stall on issue
Thus, register renaming doesn’t require reservation stations. However:
  Many modern architectures use explicit register renaming + Tomasulo-like reservation stations to control execution.

## Slide 118: Summary
Scoreboard: Track dependencies through reservations
  Simple scheme for out-of-order execution
  WAW and WAR hazards force stalls – cannot handle multiple instructions with same destination register
Reservations stations: renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards of Scoreboard
  Allows loop unrolling in HW
Dynamic hardware schemes can unroll loops dynamically in hardware
  Form of limited dataflow
  Register renaming is essential
Helps cache misses as well

## Slide 119: Summary #2
Lasting Contributions of Tomasulo Algorithm
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Pentium II; PowerPC 604; MIPS R10000; HP-PA 8000; Alpha 21264
Explicit Renaming: more physical registers than needed by ISA.
  Rename table: tracks current association between architectural registers and physical registers
  Uses a translation table to perform compiler-like transformation on the fly
With Explicit Renaming:
  All registers concentrated in single register file
  Can utilize bypass network that looks more like 5-stage pipeline
  Introduces a register-allocation problem
    Need to handle branch misprediction and precise exceptions differently, but ultimately makes things simpler
For precise exceptions and branch prediction:
  Clearly need something like reorder buffer/future file (next time)